## Slide 1: ECO FRIENDLY PORTABLE COOLING SYSTEM
TEAM: TECHNOCRATS
PROJECT ID: 39
PROJECT MODEL DEVELOPED BY MEMBERS:
NIYATI SINHA (1805501)
AAKASH KUMAR DASH (1805452)
DEEPAK KUMAR YADAV (1805483)

## Slide 2: DECLARATION
We here by declare that the details on the project entitled ' ECO FRIENDLY PORTABLE COOLING SYSTEM' submitted by us is our genuine work. And we declare that the work reported in this project has not been submitted and will not be submitted either in part or in full, by any other candidate in any exhibition.

## Slide 3: ACKNOWLEDGEMENT
It is not possible to prepare a project without the assistance and encouragement of general folks, this one is certainly no exception.
We have immense pleasure in celebrating successful completion of our model entitled, 'ECO FRIENDLY PORTABLE COOLING SYSTEM'.
We extend our gratitude to KIIT UNIVERSITY for nurturing little skill seeds to excelling talents. The idea of our project was no less than a thought that came out in the scorching summers of our hostel life.
We are also thankful to our college library and administrative staff, who directly or indirectly made us progress.
We greatly appreciate the motivation and support of our parents, who encouraged us to extend our reach.

## Slide 4: ABSTRACT
Our project aims to solve two of the major problems faced by general community, first is the lack of cheap and affordable air conditioning systems, and the other is of getting purified air.
The basic idea is based on the working of Thermoelectric coupler modules (TEC1-127xx) in which we use the physics of atoms, that an applied temperature gradient causes charge carriers in the material to diffuse from the hot side to the cold side which in turn produces a potential difference across the two sides and vice versa. This temperature difference is utilized to cool the environment.
The efficiency of our model was increased by minimizing the temperature of the hotter side, which was quite a challenging task, so we applied external eco-friendly cooling technique using water circulation through an earthen pot as well as, a normal fan in order to get the cooling system at the cheapest possible cost.

## Slide 5: INTRODUCTION
During the hot summers, almost everyone turns to the cold comfort provided by air conditioning. But what many people don’t realize – or chose to overlook – is the environmental harm air conditioning brings with it. Stan Cox, author of Losing Our Cool: Uncomfortable Truths About Our Air-Conditioned World, told The Independent,
“Air conditioning’s environmental damage is not limited to emissions of greenhouse gases and ozone-depleting chemicals. Lavish deployment of indoor climate control may indeed make it possible for us to live anywhere on the planet, but is that wise?”
Eco-friendly air conditioning is becoming more widespread as air conditioner manufacturers phase out ozone-depleting refrigerants in their products in order to meet new government regulations.
A number of technological innovations are also making AC units greener. But still these technologies stand far away from the Indian middle class society. This was a realised by us while the scrotching summers in our hostel rooms, which led us to make an air-conditioner that can serve multiple-purposes like air-filteration, dryer, and can also provide extra socket points while using eco-friendly and replenishable sources like water, earthen pot 'matka' , camphor etc and is portable and much more cheap.

## Slide 6: SOFTWARE AND COMPONENTS
SOFTWARE:
          ARDUINO IDE
          PROTEUS (SIMULATION SOFTWARE)
COMPONENTS:
          THERMOELECTRIC COUPLER(TEC-12706)
          BUCK CONVERTER(DC - DC)
          WATER PUMP
          FAN
          SMPS
          ARDUINO UNO R3
          TEMPERATURE SENSOR(DHT 11)
          LCD DISPLAY
          EARTHEN POT

## Slide 7: CHARACTERISTICS OF THERMOELECTRIC COUPLER
MAXIMUM OPERATING TEMPERATURE: 138°C
LIFE : 200,000 HOURS
SUCCESS RATE ON LONG TIME TESTING: 99.8%

## Slide 8: WORKING

## Slide 9: DESIGN OF THE MODEL
SMPS
BUCK CONVERTER
OUT AIR FLOW
CAMPHOR WALL
EARTHERN POT
OUTER-HEAT SINK
TEC-12706
AIR REGULATIONS
FAN
DISPLAY
THERMOCOL INSULATED WALLS
HS2
WATER REGULATION
T.S

## Slide 10: CIRCUIT DIAGRAMS
SMPS
Buck Converter
AC supply
TEC Module
TEC Module
LCD Display
DHT 11
(Temp. sensor)
Arduino UNO R3

## Slide 11: ADVANTAGES
ECO-FRIENDLY
PORTABLE
SMALL SIZE
LIGHT WEIGHT
USES RENEWABLE ENERGY SOURCES MAINLY
PREVENTS GLOBAL WARMING

## Slide 12: AIR PURIFICATION
PROPERTIES OF CAMPHOR
1. ANTI FUNGAL
2. ANTI BACTERIAL

## Slide 13: AIR DRYER

## Slide 14: EXTERNAL SOCKET
15A
4A
2A
2A
BUCK-CONVERTER

## Slide 15: PRICE EFFICIENT( ECONOMICAL )

## Slide 16: COMPARISION
 | NORMAL AC+DRYER+AIR PURIFIER | ECO PORTABLE COOLING SYSTEM
PRICE | 50,000 approx | 5000-6000approx
WEIGHT | 13-15KG | 1KG
COMPLEXITY | HIGH | LOW
ENVIRONMENT EFFECTS | HAZARDOUS | ECO-FRIENDLY
FRAGILITY | HIGH | LOW
MAINTENANCE COST | HIGH | VERY LOW

## Slide 17: TESTING AND DATA ANALYSIS

## Slide 18: TESTING AND DATA ANALYSIS

## Slide 19: RESULTS
We built a thermoelectric cooling system which is affordable, compact, portable, requires less maintenance, eco-friendly, easily repairable by a person from non-technical background.
It can be used by middle-class people for their personal comfort.
It also provides basic air purification and dryer facility.
The model can attain a temperature difference of roughly 12 °C, which is fairly good for a cooling system at this scale.
In tests, our model was able to reach a temperature of 21 °C inside the simulated room which was initially at 32 °C within 15 - 25 minutes. The temperature stabilizes after this.
It is highly economical.

## Slide 20: LIMITATIONS
The best part about our project is that the pros are much more significant than the cons. Mentioned below are the limitations to our model:
SMALL SCALE
WATER AVAILABILITY

## Slide 21: REFERENCES
1. ARDUINO.CC
2. PELTIER AND THOMSON EFFECT-AN OVERVIEW(SCIENCE DIRECT)
3. Camphor Effects-Indiatimes.com(Sushmita Mukherjee)
4. Losing Our Cool: Uncomfortable Truths About Our Air-Conditioned World (and Finding New Ways to Get Through the Summer) by Stan Cox (ISBN-13: 978-1595587756 , ISBN-10: 9781595587756)
5. Akram, Najath & Nirmani, H. & Jayasundere, Nisabha. (2016). A Study on Thermal and Electrical Characteristics of Thermoelectric Cooler TEC1-127 Series. 430-434. 10.1109/ISMS.2016.42.
6. Shyamu Gupta , Ankur Srivastav, Subhaan Allah, Gaurav Tiwari , , , , ."Thermoelectric Refrigeration System", Volume 6, Issue IX, International Journal for Research in Applied Science and Engineering Technology (IJRASET) Page No: 269-273, ISSN : 2321-9653, www.ijraset.com
7. Patil, R.H.. (2008). “Thermocol as thermal insulation: A key tool in implementation of energy conservation building code of India”. Journal of the Institution of Engineers (India): Architectural Engineering Division. 89. 26-30.
8. Zuccarini, Paolo & Soldani, Giulio. (2009). Camphor: Benefits and risks of a widely used natural product. Acta Biologica Szegediensis. 53. 77-82.
9. https://www.airsystems-inc.com/air-purification-news/air-quality/indoor-air-quality-and-camphor-production/
10. https://www.marlow.com/how-do-thermoelectric-coolers-tecs-work
11. https://en.wikipedia.org/wiki/Thermoelectric_cooling#Identification_and_characteristics
12. https://en.wikipedia.org/wiki/Thermoelectric_cooling

## Slide 22
WON THE FIRST PRIZE IN TECHNOVISION 2019
WON THE SECOND PRIZE IN PIC 2020 - ICDCIT
GOT PUBLISHED IN PROJECT INNOVATIONS IN DISTRIBUTED COMPUTING AND INTERNET TECHNOLOGY with ISBN: 978-93-5391-188-1
ACHIEVEMENTS

## Slide 23: THANK YOU